## Slide 1: Terminal Arrival Efficiency Rate (TAER) 101
Metric Explanation

## Slide 2
The TAER was originally designed to measure TRACON performance and the impact of Traffic Management Initiatives (TMI) within 100 miles of the airport. This is not just a measure of the approach control performance, ARTCCs ability to deliver traffic evenly also impacts this measure.
How can you influence the TAER?
Holding within 100 miles of the airport
Offloading from one arrival fix to another within 100 miles
Deviating around weather
Vectoring or speed control for spacing
Incorrect runway configurations entered into National Traffic Management Log (NTML)
Metering from ARTCC to Tracon(more consistent traffic feed)
Terminal Arrival Efficiency Rate

## Slide 3
Each day, input data is received by 0500 for the previous GMT-day from the following sources:
  Traffic Flow Management System (TFMS): Carrier, flight number, departure and arrival airport, departure (DZ) and arrival (AZ) times, Expected Departure Clearance Time (EDCT), Estimated Time Enroute (ETE).
  Aeronautical Radio, Inc. (ARINC): Carrier, flight number, leave and arrive airport, Out, Off, On, In (OOOI) times.
  Circle File from ATO Airspace Lab: Carrier, flight number, departure and arrival airport, latitude and longitude and time at 100 and 40 miles from arrival airport.
  Runway File: Runway configurations, Airport Arrival Rate (AAR), Airport Departure Rate (ADR), actual arrivals and departures by hour
  Weather Data: Instrument Approach Conditions (IAC) and Visual Approach Conditions (VAC)
Terminal Arrival Efficiency Rate (Input Data)

## Slide 4
Arrivals for Efficiency Computation – TFMS observed arrivals
  Arrival Demand – how many aircraft wanted to land during each quarter hour. The estimated wheels on time is compared to actual wheels on time to determine the number of quarters of demand for each flight. The following slides will explain how the estimated wheels on time is calculated. A single aircraft may be counted in multiple quarter hours if its expected wheels on time and actual wheels on time differ.
Efficiency Airport Arrival Rate – Number of arrivals an airport can support, which is the lesser of the Airport Arrival Rate (AAR) or Ground Delay Program (GDP) rate if one exists. Normally this would be the AAR reported in National Traffic Management Log (NTML), unless a Ground Delay Program (GDP) in effect and then the GDP program rate would be used if less than the AAR.
Terminal Arrival Efficiency Rate (Hourly TAER Calculation)
Formula:
Arrivals For Efficiency Computation
The lesser of the Arrival Demand or the Efficiency Airport Arrival Rate
Note: TAER cannot exceed 100%

## Slide 5
The Daily TAER is the sum of the hourly TAER weighted by Demand.
Terminal Arrival Efficiency Rate (Daily TAER Calculation)
Formula:
[Sum(hourly TAER * hourly Demand) ]/ [sum(hourly Demand)]
Note: TAER cannot exceed 100%

## Slide 6
For the TAER formula the “Estimated Wheels On Time” is calculated based on:
The actual 100-mile circle crossing time,
plus the estimated time from the 100-mile boundary crossing point to the 40-mile point
plus the unimpeded mean time from the 40-mile point to wheels on
These two components will be explained on the next two slides.
Terminal Arrival Efficiency Rate (Estimated Wheels On Calculation)
100-mile
40-mile
ATL

## Slide 7
Estimated time from 100-mile to 40-mile crossing point is the distance divided by the mean speed.
Distance - Based on the observed 100 mile crossing point to the nearest 40-mile boundary crossing point
Mean Speed –Average speed for the 20% of flights with the shortest distance from 100 to 40, based on 12 months of historical data for combinations of the following categories:
: - 40 mile crossing point
  - Equipment type
  - Weight class
  - Meteorological conditions (VAC or IAC)
  - Runway configuration
Terminal Arrival Efficiency Rate (Estimated Time from 100-mile to 40-mile point)
100-mile
40-mile
ATL
42
129
312
227
40 Mile
Crossing
Point

## Slide 8
Terminal Arrival Efficiency Rate (Time 40-mile point to wheels on)
40-mile Crossing Points
42
129
227
312
The 40 mile crossing points are identified for each airport using CY06 data and revalidated with CY10 data

## Slide 9
Terminal Arrival Efficiency Rate (Estimated Time 40-Mile point to wheels on)
100-mile
40-mile
ATL
42
129
312
227
The estimated time from 40-miles to wheels on is the unimpeded mean time:
Unimpeded Mean Time –
The average time for the 20% of flights with the shortest distance from 40 miles to wheels on based on 12 months of historical data for combinations of the following categories:
  40 mile Crossing Point
  Equipment type
  Weight class
  Meteorological conditions (VAC or IAC)
  - Runway configuration
40 Mile
Crossing
Point

## Slide 10
Aircraft from ELP to ATL - MD88
Arrival Runway: 26R/27L - IAC
Speed from TAER Mean Table: 429
Distance: 61
Est Time 100-40: 8.63 minutes
Unimpeded mean time from 40-Wheels On from TAER Mean Table: 15.12 minutes
Estimated Wheels On
1341z + 8.63 + 15.12 = 1405z
Actual Wheels On:
14:44
Estimated wheels on time is compared to actual wheels on time to determine the number of quarters of demand for that flight.
This flight is counted as demand for 3 quarters: 1400z-1414z, 1415z-1429z, & 1430z-1444z
Terminal Arrival Efficiency Rate (Example of how demand is calculated)
100-mile
40-mile
ATL
42
129
312
227
1341 crossed 100-mile point
Distance 61
Speed 429
Est Time: 8.63 min
Est Time: 15.12 min
40 Mile
Crossing
Point

## Slide 11
TAER calculation: Arrs for Eff / (Arr Demand or EFF AAR), whichever is lower.
EFF AAR – based on TMIs in effect, ie. GDP Rates
Terminal Arrival Efficiency Rate (TAER Hourly Report)

## Slide 12
Terminal Arrival Efficiency Rate (What Happened?)
Green dotted line – trajectory used for demand calculation
Blue line – actual route of flight

## Slide 13
Terminal Arrival Efficiency Rate (TAER Data Issues)
Next day, TAER scores are not always accurate due to incomplete data files, i.e. Arrivals for Efficiency and Demand numbers change.
  On a next day basis
    The ATO Airspace lab is processing data in real time and has not collected and assembled all the flight messages yet.
    Actual wheels on times are only available for certain carriers as provided by ARINC. Actual wheels on times for other flights are estimated based on ETMS AZ messages.
  2 days later, additional ETMS records are added and data is reprocessed. TAER scores become more accurate.
  5 days later, all the messages have been collected and properly threaded together. The TAER scores should now be more accurate.
  Approximately 40 days after the end of the month, ASQP provides actual wheels on times for additional flights. Actual wheels on times for non-ASQP, non-ARINC flights are still estimated from AZ messages.